## Slide 1
192.168.2.1/24
BD
192.168.3.1/24
192.168.4.1/24 sec
BD
demo
vrf-01
Security isolation across Bridge Domains
ESG
vmm domain
dynamic vlan allocation
EPG
Static Path 103/1/1 – vlan-30
Static Path 103/1/2 - vlan-40
EPG
192.168.1.1/24
BD
Static Path 101/1/1 – vlan-10
EPG
Static Path 102/1/1 – vlan-20
EPG
vmm domain
dynamic vlan allocation
EPG
vmm domain
dynamic vlan allocation
Static Path 104/1/1 – vlan-50
EPG
network-
segments
AP
security-
groups
AP
ESGs provides security across the VRF
Bridge Domain with multiple subnets and multiple EPGs/vlans
ACI foundational building blocks:
A Tenant provides an RBAC boundary typically linked to a business function
A VRF is mapped to a single Tenant
A Bridge Domain is mapped to a single VRF
A Bridge Domain provides one or more IP gateways (IP secondary)
An EPG is mapped to a single Bridge Domain
An EPG provides network backing and maps to:
  VMM domains + static or dynamic VLAN(s)
  Static path(s) + static VLAN(s)
An EPG defines a security boundary on a Bridge Domain
An EPG allows open communication for endpoints in the EPG, or (optionally) blocked communication for endpoints in the EPG
Inter EPG communication requires contracts (typically not required when using ESGs)
An ESG forms a security boundary on a VRF
An ESG allows open communication for endpoints in the ESG, or (optionally) blocked communication for endpoints in the ESG
Inter ESG communication requires contracts
ESG contracts supersede EPG contracts
Bridge Domain with 1x subnet and 1x EPG/vlan
Bridge Domain with 1x subnet and multiple EPGs/vlans
EPG provides security across a BD
EPG Security vs ESG Security
For your reference
Notes: Important to note that whilst ACI could use EPGs to do the policy mapping, it's never been as successful as it could have been due to customers implementing a 1:1 mapping

## Slide 2: Design Patterns
common
common.vrf-01
demo
subnet(s)
BD
VLAN
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
VLAN
(Security isolation per Bridge Domain)
EPG
Dedicated subnets for tenants with VRFs that can be (optionally) shared by different Tenants
subnet(s)
BD
common
common.vrf-01
subnet(s)
BD
demo
VLAN
(Security isolation per Bridge Domain)
EPG
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
VLAN
(Security isolation per Bridge Domain)
EPG
Typically, fewer larger subnets which can be (optionally) shared across Tenants
subnet(s)
BD
common
common.vrf-01
VLAN
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
VLAN
(Security isolation per Bridge Domain)
EPG
Used for functions which are accessible from any Tenant
Everything in the “common” Tenant is not typically seen
VRFs and BDs in “common” with EPGs and ESGs in the “user” tenant
VRFs in “common” with BDs, EPGs and ESGs in the “user” tenant
Objects in the common tenant should have unique names, e.g. common.vrf-01
Notes: The common tenant is great, however without understanding it can cause potential issues
It is strongly recommended to use unique names for objects in common to stop resolution to the wrong object
This example is often seen as it allows BDs to be shared across tenants

## Slide 3: Design Patterns
subnet(s)
BD
demo
vrf-01
VLAN
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
VLAN
(Security isolation per Bridge Domain)
EPG
Dedicated VRFs and subnets for each Tenant with Dedicated L3outs
shared-services
vrf-01
subnet(s)
BD
demo
vrf-01
VLAN
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
VLAN
(Security isolation per Bridge Domain)
EPG
Dedicated VRFs and subnets for each Tenant with Shared L3out
demo
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
test
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
common
common.vrf-01
shared-services
vrf-01
EPG and ESG in the “user” Tenant with the VRF in the “common” Tenant, and a Shared L3out in shared-services
Each Tenant has one or more network security groups
Network team controls inbound/outbound routing
Each Tenant has one or more endpoint security groups
Large subnets can be shared across Tenants
All networking constructs contained within a Tenant
Notes: option 4 requires dedicated L3out per tenant
options 5 and 6 are my personal favourites
option 5 is great when you want to provide truly dedicated network functions, the network team can manage networking and devolve control to other tenants as required. Key point is to keep L3outs etc in a dedicated tenant
option 6 is great if you've a brownfield, and/or want to have the ability to move workloads across tenants but without changing the network IP address allocation

## Slide 4
common
common.vrf-01
subnet(s)
BD
VLAN(s)
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
VLAN(s)
(Security isolation per Bridge Domain)
EPG
network-
segments
AP
VLAN(s)
(Security isolation per Bridge Domain)
EPG
VLAN(s)
(Security isolation per Bridge Domain)
EPG
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG

## Slide 5
subnet(s)
BD
subnet(s)
BD
common
common.vrf-01
demo
VLAN(s)
(Security isolation per Bridge Domain)
EPG
VLAN(s)
(Security isolation per Bridge Domain)
EPG
network-
segments
AP
VLAN(s)
(Security isolation per Bridge Domain)
EPG
VLAN(s)
(Security isolation per Bridge Domain)
EPG
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG

## Slide 6
subnet(s)
BD
subnet(s)
BD
demo
VLAN(s)
(Security isolation per Bridge Domain)
EPG
VLAN(s)
(Security isolation per Bridge Domain)
EPG
VLAN(s)
(Security isolation per Bridge Domain)
EPG
VLAN(s)
(Security isolation per Bridge Domain)
EPG
Security isolation across Bridge Domains
ESG
common
common.vrf-01
network-
segments
AP
Apps
(Optional)
AP

## Slide 7
demo
vrf-01
subnet(s)
BD
VLAN(s)
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
VLAN(s)
(Security isolation per Bridge Domain)
EPG
network-
segments
AP
VLAN(s)
(Security isolation per Bridge Domain)
EPG
VLAN(s)
(Security isolation per Bridge Domain)
EPG
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG

## Slide 8
shared-services
vrf-01
demo
vrf-01
subnet(s)
BD
VLAN(s)
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
VLAN(s)
(Security isolation per Bridge Domain)
EPG
network-
segments
AP
VLAN(s)
(Security isolation per Bridge Domain)
EPG
VLAN(s)
(Security isolation per Bridge Domain)
EPG
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG

## Slide 9
shared-services
vrf-01
subnet(s)
BD
subnet(s)
BD
common
common.vrf-01
demo
VLAN(s)
(Security isolation per Bridge Domain)
EPG
network-
segments
AP
VLAN(s)
(Security isolation per Bridge Domain)
EPG
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
test
VLAN(s)
(Security isolation per Bridge Domain)
EPG
network-
segments
AP
VLAN(s)
(Security isolation per Bridge Domain)
EPG
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG

## Slide 10
shared-services
vrf-01
subnet(s)
BD
subnet(s)
BD
common
common.vrf-01
demo
VLAN(s)
(Security isolation per Bridge Domain)
EPG
VLAN(s)
(Security isolation per Bridge Domain)
EPG
network-
segments
AP
VLAN(s)
(Security isolation per Bridge Domain)
EPG
VLAN(s)
(Security isolation per Bridge Domain)
EPG
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
test
VLAN(s)
(Security isolation per Bridge Domain)
EPG
VLAN(s)
(Security isolation per Bridge Domain)
EPG
network-
segments
AP
VLAN(s)
(Security isolation per Bridge Domain)
EPG
VLAN(s)
(Security isolation per Bridge Domain)
EPG
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG

## Slide 11: Design Patterns
common
common.vrf-01
demo
subnet(s)
BD
VLAN
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
VLAN
(Security isolation per Bridge Domain)
EPG
Dedicated subnets for tenants with VRFs that can be (optionally) shared by different Tenants
subnet(s)
BD
common
common.vrf-01
subnet(s)
BD
demo
VLAN
(Security isolation per Bridge Domain)
EPG
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
VLAN
(Security isolation per Bridge Domain)
EPG
Typically, fewer larger subnets which can be (optionally) shared across Tenants
subnet(s)
BD
common
common.vrf-01
VLAN
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
VLAN
(Security isolation per Bridge Domain)
EPG
Used for functions which are accessible from any Tenant
Everything in the “common” Tenant is not typically seen
VRFs and BDs in “common” with EPGs and ESGs in the “user” tenant
VRFs in “common” with BDs, EPGs and ESGs in the “user” tenant
Objects in the common tenant should have unique names, e.g. common.vrf-01
Notes: The common tenant is great, however without understanding it can cause potential issues
It is strongly recommended to use unique names for objects in common to stop resolution to the wrong object
This example is often seen as it allows BDs to be shared across tenants

## Slide 12: Design Patterns
subnet(s)
BD
demo
vrf-01
VLAN
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
VLAN
(Security isolation per Bridge Domain)
EPG
Dedicated VRFs and subnets for each Tenant with Dedicated L3outs
shared-services
vrf-01
subnet(s)
BD
demo
vrf-01
VLAN
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
VLAN
(Security isolation per Bridge Domain)
EPG
Dedicated VRFs and subnets for each Tenant with Shared L3out
demo
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
test
VLAN
(Security isolation per Bridge Domain)
EPG
Network
Segments
AP
Apps
(Optional)
AP
Security isolation across Bridge Domains
ESG
VLAN
(Security isolation per Bridge Domain)
EPG
subnet(s)
BD
common
common.vrf-01
shared-services
vrf-01
EPG and ESG in the “user” Tenant with the VRF in the “common” Tenant, and a Shared L3out in shared-services
Each Tenant has one or more network security groups
Network team controls inbound/outbound routing
Each Tenant has one or more endpoint security groups
Large subnets can be shared across Tenants
All networking constructs contained within a Tenant
Notes: option 4 requires dedicated L3out per tenant
options 5 and 6 are my personal favourites
option 5 is great when you want to provide truly dedicated network functions, the network team can manage networking and devolve control to other tenants as required. Key point is to keep L3outs etc in a dedicated tenant
option 6 is great if you've a brownfield, and/or want to have the ability to move workloads across tenants but without changing the network IP address allocation

## Slide 13: Tenant common
Polices
Contracts
Cont
Filters
Filt
L3out
L3out
Bridge Domains
BD
L4-7 Devices
common.vrf-01
common
shared-services
vrf-01
demo-02
demo-01
vrf-01
Bridge Domains
BD
Bridge Domains
BD
Notes: Benefits of this approach is that if I destroy the user tenant the only things that need to be cleaned are leaked routes and exported contracts

## Slide 14
common.default
Cont
common
demo
vzAny
P
C
CCI
vzAny
P
C
CCI
All EPGs
P
C
I
CCI
EPG
P
C
I
CCI
All ESGs
P
C
I
CCI
ESG
P
C
I
CCI
All extEPGs
P
C
I
CCI
extEPG
P
C
I
CCI
L3out
L3out
vrf-01
Notes: Benefits of this approach is that if I destroy the user tenant the only things that need to be cleaned are leaked routes and exported contracts

## Slide 15
common.default
Cont
common
demo
vrf-02 (internal)
vzAny
P
C
CCI
vzAny
P
C
CCI
All EPGs
P
C
I
CCI
EPG
P
C
I
CCI
All ESGs
P
C
I
CCI
ESG
P
C
I
CCI
All extEPGs
P
C
I
CCI
extEPG
P
C
I
CCI
L3out
L3out
vrf-01 (external)
Route leaking between VRFs
Notes: Benefits of this approach is that if I destroy the user tenant the only things that need to be cleaned are leaked routes and exported contracts

## Slide 16
common.default
Cont
common
shared-services
vrf-01 (internal)
vzAny
P
C
CCI
vzAny
P
C
CCI
All EPGs
P
C
I
CCI
EPG
P
C
I
CCI
All ESGs
P
C
I
CCI
ESG
P
C
I
CCI
All extEPGs
P
C
I
CCI
extEPG
P
C
I
CCI
L3out
L3out
vrf-01 (shared external)
demo
Route leaking between VRFs
Notes: Benefits of this approach is that if I destroy the user tenant the only things that need to be cleaned are leaked routes and exported contracts

## Slide 17
permit-to-core-services
Cont
vzAny
P
C
CCI
vzAny
P
C
CCI
All EPGs
P
C
I
CCI
EPG
P
C
I
CCI
All ESGs
P
C
I
CCI
ESG
P
C
I
CCI
All extEPGs
P
C
I
CCI
extEPG
P
C
I
CCI
L3out
L3out
demo
vrf-02 (internal)
vrf-01 (external)
Route leaking between VRFs
core-services
P
C
I
CCI
EPG
P
C
I
CCI
Notes: Benefits of this approach is that if I destroy the user tenant the only things that need to be cleaned are leaked routes and exported contracts