## Slide 1: NXOS – Interfaces configured on switch by switch basis
vrf-01
192.168.150.0_24
SVI
VLAN150
VLAN
192.168.151.0_24
SVI
VLAN151
VLAN
192.168.152.0_24
SVI
VLAN152
VLAN
192.168.153.0_24
SVI
VLAN153
VLAN
192.168.154.0_24
SVI
VLAN154
VLAN
192.168.155.0_24
SVI
VLAN155
VLAN
192.168.156.0_24
SVI
VLAN156
VLAN
eth101/1/1
switchport access vlan 150
Int
eth101/1/2
switchport access vlan 156
Int
eth101/1/3
switchport access vlan 154
Int
eth102/1/1
switchport access vlan 155
Int
eth102/1/2
switchport access vlan 154
Int
eth102/1/3
switchport access vlan 152
Int
eth103/1/1
switchport access vlan 156
Int
eth103/1/2
switchport access vlan 151
Int
eth103/1/3
switchport access vlan 153
Int
eth104/1/1
switchport access vlan 154
Int
eth104/1/2
switchport access vlan 151
Int
eth104/1/3
switchport access vlan 153
Int
eth105/1/1
switchport access vlan 152
Int
eth105/1/2
switchport access vlan 156
Int
eth105/1/3
switchport access vlan 151
Int
eth106/1/1
switchport access vlan 153
Int
eth106/1/2
switchport access vlan 155
Int
eth106/1/3
switchport access vlan 151
Int
eth107/1/1
switchport access vlan 152
Int
eth107/1/2
switchport access vlan 155
Int
eth107/1/3
switchport access vlan 151
Int
eth108/1/1
switchport access vlan 150
Int
eth108/1/2
switchport access vlan 150
Int
eth108/1/3
switchport access vlan 155
Int
101
102
103
104
105
106
107
108
201
202
203
204

## Slide 2: ACI– Interfaces configured on VLAN by VLAN basis
vrf-01
192.168.150.0_24
BD
VLAN150
eth101/1/1
eth108/1/1
eth108/1/2
EPG
192.168.151.0_24
BD
VLAN151
eth103/1/2
eth104/1/2
eth105/1/3
eth106/1/3
eth107/1/3
EPG
192.168.152.0_24
BD
VLAN152
eth102/1/3
eth105/1/1
eth107/1/1
EPG
192.168.153.0_24
BD
VLAN153
eth103/1/3
eth104/1/3
eth106/1/1
EPG
192.168.154.0_24
BD
VLAN154
eth101/1/3
eth102/1/2
eth104/1/1
EPG
192.168.155.0_24
BD
VLAN155
eth102/1/1
eth106/1/1
eth107/1/2
eth108/1/3
EPG
192.168.156.0_24
BD
VLAN156
eth101/1/2
eth103/1/1
eth105/1/2
EPG
101
102
103
104
105
106
107
108
201
202
203
204
AP
my-vlans
demo
my-business-unit
VLAN folder
Business unit folder

## Slide 3: Focus on the Interface Policy Group
esx-hosts-vSwitch-0
Interfaces > Leaf Interfaces > Policy Groups
cdp—enabled
Policies > Interface
esx-hosts-vSwitch-0
Policies > Global > AAEP
esx-hosts-vSwitch-0
Physical Domain
esx-hosts-vSwitch-0
Pools > VLAN Pool
leaf-101
Switches > Leaf Switches > Profiles
leaf-101
Interfaces > Leaf Interfaces > Profiles
esx-hosts-vSwitch-0
Access Port Selector
leaf-102
Switches > Leaf Switches > Profiles
leaf-102
Interfaces > Leaf Interfaces > Profiles
esx-hosts-vSwitch-0
Access Port Selector
The Interface Policy Group (template) is the definition of the interface settings for a device attaching to the fabric
eth1/1, eth1/2
Port Blocks
eth1/1, eth1/2
Port Blocks
Leaf Profiles define a logical representation of a Leaf switch
The Access Port Selector applies the Policy Group to a logical Leaf switch
Port Blocks identify the interfaces which will be configured
Switch Profiles identify one or more Leaf switches
Interface Polices which are aggregated into a Policy Group
An AAEP maps the VLANs from a VLAN pool to an interface Policy Group, and ultimately to an interface. In traditional Nexus this would be like the command “switchport trunk allowed vlan…”
A Domain defines where VLANs can be consumed
A VLAN pool is a list of one or more VLANs
Physical
Logical

## Slide 4: Focus on the Interface Policy Group
esx-hosts-vSwitch-0
Interfaces > Leaf Interfaces > Policy Groups
cdp-enabled
Policies > Interface
esx-hosts-vSwitch-0
Policies > Global > AAEP
esx-hosts-vSwitch-0
Physical Domain
esx-hosts-vSwitch-0
Pools > VLAN Pool
leaf-101
Switches > Leaf Switches > Profiles
leaf-101
Interfaces > Leaf Interfaces > Profiles
esx-hosts-vSwitch-0
Access Port Selector
leaf-102
Switches > Leaf Switches > Profiles
leaf-102
Interfaces > Leaf Interfaces > Profiles
esx-hosts-vSwitch-0
Access Port Selector
The Interface Policy Group (template) is the definition of the interface settings for a device attaching to the fabric
eth1/1, eth1/2
Port Blocks
eth1/1, eth1/2
Port Blocks
Physical
Logical

## Slide 5: Focus on the Interface Policy Group
esx-hosts-vSwitch-0
Interfaces > Leaf Interfaces > Policy Groups
cdp-enabled
Policies > Interface
esx-hosts-vSwitch-0
Policies > Global > AAEP
esx-hosts-vSwitch-0
Physical Domain
esx-hosts-vSwitch-0
Pools > VLAN Pool
leaf-101
Switches > Leaf Switches > Profiles
leaf-101
Interfaces > Leaf Interfaces > Profiles
esx-hosts-vSwitch-0
Access Port Selector
leaf-102
Switches > Leaf Switches > Profiles
leaf-102
Interfaces > Leaf Interfaces > Profiles
esx-hosts-vSwitch-0
Access Port Selector
The Interface Policy Group (template) is the definition of the interface settings for a device attaching to the fabric
eth1/1, eth1/2
Port Blocks
eth1/1, eth1/2
Port Blocks
Physical
Logical
Interface Polices which are aggregated into a Policy Group
An AAEP maps the VLANs from a VLAN pool to an interface Policy Group, and ultimately to an interface. In traditional Nexus this would be like the command “switchport trunk allowed vlan…”
A Domain defines where VLANs can be consumed
A VLAN pool is a list of one or more VLANs

## Slide 6: Focus on the Interface Policy Group
esx-hosts-vSwitch-0
Interfaces > Leaf Interfaces > Policy Groups
cdp-enabled
Policies > Interface
esx-hosts-vSwitch-0
Policies > Global > AAEP
esx-hosts-vSwitch-0
Physical Domain
esx-hosts-vSwitch-0
Pools > VLAN Pool
leaf-101
Switches > Leaf Switches > Profiles
leaf-101
Interfaces > Leaf Interfaces > Profiles
esx-hosts-vSwitch-0
Access Port Selector
leaf-102
Switches > Leaf Switches > Profiles
leaf-102
Interfaces > Leaf Interfaces > Profiles
esx-hosts-vSwitch-0
Access Port Selector
The Interface Policy Group (template) is the definition of the interface settings for a device attaching to the fabric
eth1/1, eth1/2
Port Blocks
eth1/1, eth1/2
Port Blocks
Physical
Logical
Interface Polices which are aggregated into a Policy Group
An AAEP maps the VLANs from a VLAN pool to an interface Policy Group, and ultimately to an interface. In traditional Nexus this would be like the command “switchport trunk allowed vlan…”
A Domain defines where VLANs can be consumed
A VLAN pool is a list of one or more VLANs
Leaf Profiles define a logical representation of a Leaf switch
Switch Profiles identify one or more Leaf switches

## Slide 7: Focus on the Interface Policy Group
esx-hosts-vSwitch-0
Interfaces > Leaf Interfaces > Policy Groups
cdp-enabled
Policies > Interface
esx-hosts-vSwitch-0
Policies > Global > AAEP
esx-hosts-vSwitch-0
Physical Domain
esx-hosts-vSwitch-0
Pools > VLAN Pool
leaf-101
Switches > Leaf Switches > Profiles
leaf-101
Interfaces > Leaf Interfaces > Profiles
esx-hosts-vSwitch-0
Access Port Selector
leaf-102
Switches > Leaf Switches > Profiles
leaf-102
Interfaces > Leaf Interfaces > Profiles
esx-hosts-vSwitch-0
Access Port Selector
The Interface Policy Group (template) is the definition of the interface settings for a device attaching to the fabric
eth1/1, eth1/2
Port Blocks
eth1/1, eth1/2
Port Blocks
Physical
Logical
Interface Polices which are aggregated into a Policy Group
An AAEP maps the VLANs from a VLAN pool to an interface Policy Group, and ultimately to an interface. In traditional Nexus this would be like the command “switchport trunk allowed vlan…”
A Domain defines where VLANs can be consumed
A VLAN pool is a list of one or more VLANs
Leaf Profiles define a logical representation of a Leaf switch
Switch Profiles identify one or more Leaf switches
The Access Port Selector applies the Policy Group to a logical Leaf switch
Port Blocks identify the interfaces which will be configured

## Slide 8
esx-hosts-vSwitch-0
Interfaces > Leaf Interfaces > Policy Groups
cdp-enabled
Policies > Interface
esx-hosts-vSwitch-0
Policies > Global > AAEP
esx-hosts-vSwitch-0
Physical Domain
esx-hosts-vSwitch-0
Pools > VLAN Pool
esx-hosts-vSwitch-0
Access Port Selector
esx-hosts-vSwitch-0
Access Port Selector
esx-hosts-vSwitch-0
Access Port Selector
esx-hosts-vSwitch-0
Access Port Selector
esx-hosts-vSwitch-0
Access Port Selector
esx-hosts-vSwitch-0
Access Port Selector
esx-hosts-vSwitch-0
Access Port Selector
esx-hosts-vSwitch-0
Access Port Selector
eth1/1
eth1/2
Port Blocks
eth1/1
eth1/2
Port Blocks
eth1/6
eth1/7
Port Blocks
eth1/6
eth1/7
Port Blocks
eth1/23
eth1/24
Port Blocks
eth1/23
eth1/24
Port Blocks
eth1/41
eth1/42
Port Blocks
eth1/41
eth1/42
Port Blocks
The Interface Policy Group (template) is the definition of the interface settings for a device attaching to the fabric